Table of Contents

І. Summary

1. Basic function of the alarm host ......................................... 2

2. Main technical specification................................................2

3. Alarm system basic configuration ............................................3

4. Optional configuration ....................................................3

П．Structure and installation of the alarm host

1.Installation of the alarm host ...................................................4

1.1 Telephone line and power cord connection  ........................................5

2.wireless detector installation ..........................................6

Ш、Setting and usage of the alarm host

1. The basic setting of the alarm host ........4

2. Coding between main host and wireless detector .................................... 14

3 .To arm the alarm host ........................................... 14

4. Trigger to alarm ............................................ 15

5. Alarm center operation.................................................. 16

6. Remote control operation.............................................. 17

7. System reset ........ ......................................... 17

8. Setting and usage of the wireless siren .................................. 18

І. Summary

Thank you for purchasing our alarm system ,in order to enable you to use this products correctly and quickly ,please read this manual carefully before to use .

Our alarm system belong to a new generation of intelligent alarm system ,has made a dramatic improvement on the basis of the previous alarm system according to the users’ complaints .Contrast as follows ：

1)The battery of Original infrared detector can only use 6-12  months ;now the new infrared detector battery can use for 3 years at the most .

2）.When the original detector has low battery ,the owner do not know initiative; now the new infrared detector can dial the owner number to inform when there is a low battery  ,and through the voice message to inform which detector need to change the battery in time .

3）.The original infrared detector is signal trigger alarm; new infrared detector adopts human behavior identification ,make sure it’s human then alarm ,effectively reduce the misstatement happens .

4）The original alarm host only support small wire siren ;New alarm host support small wire siren and wireless siren .

１.Detailed basic function of the alarm host

- Double LED digital display ,Visual display alarm defence zone ,keyboard input content

- Keyboard operation ,easy and applicable

- Voice prompt function ,arm ,disarm or keyboard programming has voice prompt.

- Password operation ,Make sure the system is safe .

5) Can connect with our company receiving alarm platform ,achieve networking management .

6) Can presetting 4 groups of alarm phone number and 2 groups of alarm center number ,2 groups of detector low battery prompt numbers .

7) Can control the alarm host arm ,disarm and listen in by calling the alarm host number .

8) Has voice prompt function when alarming or operating from long distance .

9).Alarm host has the priority to make alarm phone calls when the telephone is being using,And telephone line fault detection function .

10)Using the learning code to add wireless detector ,easy to register .

11)Alarm host has build-in wireless transmitter module (optional ), support wireless siren (optional )

12)Arm or disarm with alarm tone

13.Build in battery ,Automatic switching when power off .

2.Technical Parameters :

- Power supply ：DC9V（300mAh）

- Backup battery ： 7.2V(1.2V x6 ) Ni-MH rechargeable battery

- Work current ：　Daily duties ：《10mA, alarm communication 《300mA（Build-in siren ，Open the wireless siren）

- Wireless frequency: Receive 315MHz( emission 433 MHz）

- Wireless encoding ：ASK

- Wireless receive sensitivity: -105dBm@12dB SINAD

- Wireless zone number ：99

- alarm numbers ： 8 group (Include 2 groups of center number ，6 groups of alarm number  )

- External alarm volume : ≥110dBspl

- Working temperature ： -15℃～ +55℃  Relative humidity ≤90%

3.Alarm system Basic configuration :

1) Alarm host ( with back-up battery inside )   1 PC

2) Wireless pet immunity infrared detector  1 PC

3)Wireless door sensor                      1 PC

4)Wireless remote controller                 2 PCS

5)Wire siren                              1 PC

6)English User manual                      1 PC

7)Power supply                             1PC

8)Telephone line                            1 PC

9)Warranty Card                            1 PC

4.Optional configuration

1）Wireless intelligent infrared detector

2）Wireless smoke detector ,wireless gas detector etc

3）Wireless siren

4）wired or wireless infrared fence and beam detector ]

П．Installation of the alarm host

- Alarm host installation

Alarm host appearance

- Telephone line and power connection

There are two telephone line interface on the telephone host ,the top one is incoming line port ,another one is out line port ,incoming line port  connect with outside telephone lines ,out line port connect with telephone

Attention : if the telephone connect with the network MODEM ,then the MODEM must connect with outlet port ,otherwise will affect the alarm host dial alarm numbers .As shown below :

- Wireless detectors device installation

- Magnetic door/window installation

The principle of magnetic door detector is induction the distance between the magnetron and  magnet , when the gap of magnet and magnetron is increased to a certain distance, the detector can induction it .then launch the signal to alarm. Fix it on the door or window ,can detect the open or close of the door or  window ,Separately install the magnet and emitter on the door and  doorframe ,use adhesive tape and screw to fixe it .

The door detector has low power voice prompt function ,belong to new generation detectors .

- Infrared detector installation

Passive infrared detector using infrared wavelengths to sense the temperature change to make sure the human activities. Detection range from 5 to 8 M, detection angle is level 110,vertical 60.Fix the infrared on the wall ,2-2.2 meters away from the ground ,adjust the angle ,face the area which need to detect .

Attention: Infrared detector  has installed appropriate or not ,directly affect the accuracy of the alarm .Please inquiry the supply before install ,in order to avoid misstatement and omission .

The infrared detector using intelligent discriminant way ,can effectively prevent misstatement ,also has low power alarm and anti-tamper function ,belong to new generation detectors.

- Wireless remote controller usage

The remote controller has four buttons：

Away arm button，Home arm button，Disarm button，Panic button 。

- Press AWAY ARM button， Alarm host with voice prompt “away armed “,Execute delay arm, ”away indicator light flashing for 30 seconds ,then light on ,Enter arm state.

- Press AWAY ARM button+ PANIC BUTTON ，enter into arm state ,away indicator light on.

- Press HOME ARM button，Voice prompt “home armed”， Execute  delay arm，“home” indicator light flash for 30 seconds ,then the light on .enter into home  arm state .

- Press HOME ARM  button+ PANIC BUTTON ，Enter inter arm state immediately ，home indicator light on .

- When press the PANIC BUTTON  ，no matter what state the alarm host in ,arm or disarm ,the alarm host will alarm. the alarm indicator light will on at the same time .

- Press DISARM button  will disarm the alarm host ，immediately terminate ongoing alarm operation .

Attention : In home arm state ,the detector  in “home” mode when registered , will alarm ; in “away” mode  when registered , will not alarm .

In away arm state , no matter in home or away mode when registered ,the detectors will alarm .

Ш、Setting and usage of the alarm host

- Alarm host basic setting

Alarm host must do some necessary settings before use .then the system can work in a normal working condition .

When start to set ,In lock state ,must input the password to unlock the keyboard .the initial password is 1234 ,There is "PP " display after the input the correct password ,Then can carry out arm or disarm setting and other operations .

Keyboard will automatically locked when there is no any operations on the keyboard for 15 seconds.

In unlock state ,When press the PROGRAM key ,voice prompt with “System is in registration state “,LED digital tube display "- -",can input instruction for corresponding settings on the keyboard .When one instruction has completed ,LED digital tube display " - - ".No need to quit the program state ,can move to next instruction setting .If do not want to save the setting during operation ,or setting has completed ,Directly press “BACK ‘ key to quit the setting state .Voice prompt with “System is quitting registration state “when quit .

Detailed instructions and setting as follows :

（Attention: All instructions must operate in programming state ）

- Setting alarm center  number

（This number will automatically dial when there is an alarm ,to inform alarm center, if the user didn’t connect with the networking system platform, please do not set this number ,otherwise will continuously to call this number, affect the speed of user to dial the other numbers .

Operation instruction :

Telephone number + * # + serial number (8 or 9 )

There is "DI" sound  or"Registered complete"voice prompt after input .System will save automatically .And back to program state ,Input other instructions to carry out other settings .

Description : 8 or 9 means the first alarm center number or the second alarm center number .

To delete the alarm center number ,Only need to input * # 8 or * # 9 in program state .If need to change ,Input a new telephone number according to the instructions .

- Setting user alarm number

（Alarm host will automatically dial this number to inform the user when there is an alarm . ）

Operation instruction :

Telephone number + * # + serial number (1 - 4  )

There is "DI" sound  or"Registered complete"voice prompt after input .System will save automatically .And back to program state ,Input other instructions to carry out other settings .

Description : 1 - 4 means the first to the fourth of the user alarm numbers .

To delete the user alarm number ,Only need to input * # 1 - 4 in program state .If need to change ,Input a new telephone number according to the instructions .

- Setting detector low battery prompt numbers

(In the case when the detectors have low battery ,alarm host will automatically dial the number to inform the user )

Operation instruction :

Telephone number + * # + serial number (5 - 6)

There is "DI" sound  or"Registered complete"voice prompt after input .System will save automatically .And back to program state ,Input other instructions to carry out other settings .

Description : 5 #  or 6 # means the first  and the second detector low battery prompt telephone numbers .

To delete the user alarm number ,Only need to input * # 5 - 6 in program state .If need to change ,Input a new telephone number according to the instructions .

- Setting system password

Operation instruction ：

Password + * # + 7

There is "DI" sound  or"Registered complete"voice prompt after input .System will save automatically .And back to program state ,Input other instructions to carry out other settings .(System initial password : 1234 )

- Setting user ID ( Host ID or User ID )

（Alarm host connect with alarm center ,When send alarm information to alarm center , need identify the user code ,or host ID ,user ID）

Operation instruction ：

CODE +* # + 0

There is "DI" sound  or"Registered complete"voice prompt after input .System will save automatically .And back to program state ,Input other instructions to carry out other settings .(System initial value  : 0001 )

- Setting remote control answering ring times

Operation instruction ：

007 * * 1 X X #

X X means  setting times ( 01 - 08 ) .Times can't  more than 08 ( the  maximum of telecom operation  times  ),otherwise can't get through ,There is "DI" sound  or"Registered complete"voice prompt after input .System will save automatically .And back to program state ,Input other instructions to carry out other settings .

- Setting time of siren

Operation instruction ：

007**2XX#

XX means  the setting siren time (01- 30 mins )

There is "DI" sound  or"Registered complete"voice prompt after input .System will save automatically .And back to program state ,Input other instructions to carry out other settings .

- Setting telephone line detect disconnection function ,ON or OFF

( This function on ,the siren will on when the telephone line is off or line has failed ）

Operation instruction ：

007**010#（OFF），011#（ON）

Input 007**010# means close the telephone line detection function ;007**011#  means open the telephone line detection function .

There is "DI" sound  or"Registered complete"voice prompt after input .System will save automatically .And back to program state ,Input other instructions to carry out other settings .(System default this function ON )

- Setting siren ON or OFF when there is a emergency alarm

（This function can set the siren ON or OFF ,when use the panic button or remote controller for emergency alarm）

Operation instruction ：

007**020#（OFF），021#（ON）

Input 007**020#  ,When there is an emergency alarm ,the siren will not sound ,007**021# ,when there is an emergency ,the siren will sound .

There is "DI" sound  or"Registered complete"voice prompt after input .System will save automatically .And back to program state ,Input other instructions to carry out other settings .(System default this function ON )

- Setting wireless alarm function ON or OFF

（On the premise that the alarm host work with our factory wireless siren ,Can control the wireless siren ON or OFF by this setting .

Operation instruction ：

007**030#（OFF），031#（ON）

Input 007**030# means close the wireless siren function ,Input 007**031# means open the wireless siren function

There is "DI" sound  or"Registered complete"voice prompt after input .System will save automatically .And back to program state ,Input other instructions to carry out other settings .(System default this function OFF )

- Setting wireless Siren voice prompt ON or OFF when arm  and disarm

( This function can set the wireless siren voice prompt ON or OFF when arm or disarm the alarm host )

Operation instruction ：

007**040#（OFF），041#（ON）

When input 007**040# ,means close the wireless siren prompt voice when arm and disarm ;Input 007**041# ,means open the wireless siren voice prompt when arm and disarm .When this function on ,there is a short beep voice prompt when arm or disarm .

There is "DI" sound  or"Registered complete"voice prompt after input .System will save automatically .And back to program state ,Input other instructions to carry out other settings .(System default this function ON )

- Wireless siren code instruction

Operation instruction ：

007**10#

The alarm host will launch the wireless alarm signal to register after input this instruction .Press BACK key to exit program state .

- Query alarm center or user number ,password and user ID .

Operation instruction ：

007**X#  （X=0-9）

X  means  any number inside 0-9，The serie number is the same like the user number .alarm center number ,User ID ,and password series number ,Such as 007**1# mean inquiry the user ID . after input the instructions ,the numbers will show on the system LED digital tube ,With voice prompt at the same time .

- The learning code of wireless detector and remote controller

In standby mode , by pressing the top of the host coding key for learning code to wireless remote controller and wireless detectors .

- First time to code : Press the CODE key for 2-3 seconds ,the alarm host will voice prompt “System is in registration state “,The zone on the LCD display will show “ 01 “ ,Can change the zone by press the number on the panel .Press “HOME ARM “ or AWAY ARM “to choose alarm type .then trigger the detector to alarm .The alarm host will voice prompt “Registered complete “ after receive the signal from the detectors or remote controllers .Then if press the “BACK “ key or “CODE “ key ,means exit the code state .If need code other detectors ,no need to exit ,according to the above method directly input the zone number ,then choose the alarm type to learning code ,until the code is completed ,then press the “BACK “key or “CODE “key to exit the code state .

Add detectors code :  If need add detectors or remote controllers ,and do not want to delete the exiting detectors or remote controllers code ,can add code by learning code .as follows :

First click the CODE key ,then press it again for 2-3 seconds ,the alarm host will voice prompt “System is in registration state “,Then use the first time code way to choose zone and alarm type to learning code .

Clear the code : System need initialization to clear the code

Attention : In HOME ARM state ,the detector will alarm when choosed the HOME  type to code .In AWAY type when code ,will not alarm .

In AWAY ARM ,no matter in HOME or AWAY type when code ,the detectors will alarm .

3.　ARM alarm host  ( AWAY ARM and HOME ARM mode )

Method one :

ARM by host panel

A     AWAY ARM : Input system password ,then press “AWAY ARM ”,host will voice prompt “AWAY ARM “,”AWAY “indicator light will flash ,After 30 seconds ,the light will on ,means system has enter into away arm state

HOME ARM : Input system password ,then press “HOME ARM” key ,host will voice prompt “HOME ARM ”,”HOME” indicator light will flash ,After 30 seconds the light will on .means system has enter into home arm state

Method two :

ARM by wireless remote controller  (Please refer to the former “usage of wireless remote controller )

Method three :

ARM by phone from remote

As follows : Using mobile phone or telephone to call the telephone which connect to the alarm host .when it has reached the setting ring times ,alarm host will automatically connect ,Input the password when there is a voice prompt ask to input password  .There is voice prompt when the password is correct , “Press 1 for arm; Press 2 for disarm ; Press 5 for listen in ; press 6 for unlock ;please press # for dismiss the alarm  ; Hang up to quit “If password is wrong ,voice prompt with “Password is not correct, please input again “ .When the Password is correct ,Enter 1 for arm the host ,enter 2 to disarm the host .

Attention : In HOME ARM state ,the detector will alarm when  choosed the HOME  type to code .In AWAY type when code ,will not alarm .

In AWAY ARM ,no matter in HOME or AWAY type when code ,the detectors will alarm .

4　Alarm trigger action

Method one :

In ARM state ,alarm host will trigger alarm  by all kind of detectors .

Method two :

In any state , belong to emergency alarm detector type will trigger to alarm (such as smoke detector ,gas detector ,panic button and so on )

Method three :

In any state , Press the emergency button  on the wireless remote controller will trigger to alarm (already registered with the alarm host )

When alarming ,LED digital tube will display the alarm zone number ,the alarm indicator light will on at the same time .

5.　Alarm operation :

- Alarm call setting

When the alarm host is alarming , it will dial the setting alarm phone number in order ,when the alarm call has been connected ,The alarm host will play the voice prompt ,and inform the alarm type .User can input the corresponding number to operation .(there is 6 voice prompt ,but press 6 will not unlock )

Press “1 “ for arm

Press “2 “ for disarm

Press “5 “ for listen in

Press “# “ for hang up , end up this alarm ,means dismiss this alarm .But the host state will not change .

Do not enter any numbers and directly hang up , Alarm host will dial next alarm phone number

Attention : When connected to the alarm host ,If no any operations for 30 seconds ,the alarm host will hang up automatically ,and dial the next alarm phone number .

  - Disarm by remote controller

Press the disarm button on the remote controller when dialing the alarm phone number , will terminate the current alarm operation .

3）        Disarm by alarm panel .

Input the password to unlock the keyboard ,Then press the “BACK/DISARM” key , mean disarm .

4） Alarm timeout ,automatically exit .

If the alarm host has dialed all of the alarm phone numbers for 5 times in a row , still no effective alarm or disarm ,The alarm host will not dial any alarm phone number ,exit the alarm and enter the standby mode .

- Remote control function operation

Using telephone or mobile to dial the connected phone ,alarm host will connect automatically ,the alarm host will voice prompt to enter the password and doing corresponding operations ,Users have to enter the password  ,enter into function setting operation after the password is correct .Pressing the follow keys can do the corresponding operations :

1 	ARM；

2	DISARM；

5 	LISEN IN ；

#        Hang up and exit remote control operation

Hang up after operation ,Exit

Attention : Doing the above operations ,If the host voice prompt “wrong password,please input again “,should re-enter the password again .

- System reset :

When need to restore the system to factory settings ,can use the system reset function,reset as follow :

Turn off the alarm first ,then turn on ,Input "0000"after 6 seconds ,The system will voice prompt " System Initialization complete ",means reset successful .

- Wireless siren learning code and usage

  - Learning code between the wireless siren and alarm host

First , the host in the program state ,please input 007* * 10 #  instruction to launch wireless signal ,

Plug in the wireless siren power supply ,One “beep “ sound means the wireless siren is ready to work ,then plug off the power supply ,then plug in again ,at this time ,siren with no any sound ,plug off the power supply then plug in again ,then the wireless siren will make “beep,beep ,beep “prompt sound ,this mean siren register complete ,Simple steps as follows :

Power on (beep)---power off then power on (no beep)---power off then power on (beep ,beep beep) code successfully ,Every step time interval is 1-2 seconds .

- Wireless siren usage

When the siren has registered complete ,power on ,the siren will make “beep beep “two sound when arm or disarm the alarm host ,when alarm host alarming ,the siren will make a continuous sound .

Thanks for reading our manual ,any questions please contact our after-sales service .‘

LED Voice Prompt

Intelligent Anti-theft Alarm System